## Slide 1: Formation Control: A Centralized and Decentralized Approach
Notes: Brief Introduction - don’t need to introduce ourselves, it just sounds awkward
Mention both centralized and decentralized formation control

## Slide 2: Centralized vs Decentralized
In both cases we launch the arena as usual
Centralized approach runs a single controller with global knowledge
Decentralized approach runs a controller per robot
  Each robot acts individually
A ‘leader’ robot sends messages with its state to connected robots
Other ‘followers’ update their belief of the leader and relay this message
Notes: Both cases start by launching a ros world the same way
Centralized approach runs a single program that acts based on global knowledge - knows every robot’s state
Decentralized approach has every robot act individually and participate in message passing to spread leader’s state
Knowledge of the leader is enough to get our robots back in formation with our leader-referenced scheme (explained later) - mention we pass messages on links

## Slide 3: Formations
Line
Column
Diamond
Wedge
Notes: Discuss how we implement formations here - one robot is the center, the others have relative positions from the center
Mention the links for message passing in decentralized solution - leader sends state (pose and sensor measurements) and followers store and relay it

## Slide 4: Behavior-based control
Formation Maintenance
Goal Navigation
Static Obstacle Avoidance
Dynamic (Robot) Obstacle Avoidance
T. Balch and R. C. Arkin, Behavior-based Formation Control for Multi-robot Teams
Notes: Paper was the basis of our work
Compute vectors for each robot for formation, goal, obstacle avoidance

## Slide 5: Extending the Paper
Behavior approach was designed for open worlds
Added formation switching strategy
Robots move as a column in tight areas (corridors)
Notes: Explain that the approach in the paper was for open worlds
Added the ability to detect corridors and tight areas using sensor measurements
Move into column formation until free again as its the narrowest formation

## Slide 6: Formation Maintenance Vector
First find the desired formation position and orientation
Two methods:
Unit-Reference - Average all robot positions to find centre of formation
  Requires many messages when decentralized
Leader-Reference - Leader is considered always in formation
  Followers compute their vector to get in formation
  Easier to implement in a decentralized system
Notes: Explain unit-reference and why we didn’t do it - decentralized unit-reference requires global knowledge of all robot positions and lots of messages
Explain leader-reference - a leader robot is center of formation and the other followers compute a vector, formation offsets are rotated and translated onto the leader
Decentralized leader-reference is easier as only need the leader’s state

## Slide 7: Formation Maintenance Vector
Scale vector magnitude based on distance
Dead Zone: magnitude = 0
Control Zone: magnitude scaled linearly
Ballistic Zone: magnitude = 1
Notes: Explain the zones: dead zone = 1.5 * robot radius (1.5 * 0.0525), control zone = dead zone + spacing distance (0.3), ballistic zone outside this

## Slide 8
Notes: Show robots in random places, get into formation
Robots go through each formation as they move
Undergo an orthogonal rotation lmao

## Slide 9: Goal Navigation Vector
The Leader computes RRT* path to some goal position
  This computes a safe path for the leader only
Only the leader has a goal vector
Followers just keep formation
Notes: Followers do not need a goal velocity
Leader runs RRT* for an obstacle free path (very briefly say we sample points, add to tree, rewire based on cost)
Mention that we can store the path to avoid computation costs in the future (makes for good evaluation argument)

## Slide 10: Insert video 4
Notes: Robots navigate a path with tight corners and turns

## Slide 11: Static Obstacle Avoidance Vector
Mix of braitenberg/rule-based controllers
Robot sensors do not distinguish robots and obstacles
Leader slows down when robots are avoiding obstacles
Split and Merge
Robots pick a preferred side for moving around an object depending on their position in formation
Notes: Mention braitenberg for centralized and rule-based for decentralized, since braitenberg is enhanced to account for all robot positions
Can say lasers are poor against other robots in practice
Robots have the formation velocities switched for goal velocities sometimes, so they can move in the right direction without falling into an obstacle, keeps it robust.

## Slide 12: Dynamic (Robot) Obstacle Avoidance Vector
Compute an ‘on-off’ vector that stops moving a robot when:
  They get close
  They face each other
O(n2) as we consider robots in pairs, stop the one with lowest ID, to prevent deadlock
Notes: Explain robot avoidance weights as stopping a robot from moving, includes how in-front of each other they are, and is efficient

## Slide 13: Insert video 2
Notes: Robots split and merge around obstacles
Split around obstacles and merge back into formation

## Slide 14: Weighted Combination
Overall velocity vector computed as a weighted sum of goal, formation, obstacle avoidance and noise vectors
Apply ‘rules’ to filter spurious/erroneous velocities:
  Robots stop if they are about to collide with another robot
  Robots stop at the goal
  Leader can slow down if followers not in formation
Notes: Explain how weights affect the relative contribution and behavior, leading to split-and-merge, with 5% noise to avoid minima
Mention our weights (.35 goal, .2 formation, .22 obstacles)
Mention how robot avoidance weights are used, how we stop spurious movement if at goal, and how we slow the leader so others can catch up (scale by .3)

## Slide 15: Insert video 3
Notes: Robots navigate to goal and split and merge around obstacle and into formation
Achieved with weighting obstacle avoidance higher than formation to get the split

## Slide 16: Formation Switching
Use robot sensors to detect tight gaps
Centralized: Switch formation if leader (or majority of robots) detect a tight gap
Decentralized: Only the leader sensors are used
Formation becomes a column
Notes: Explain the use of robot sensors to detect enclosed space on the sides to determine a corridor (within .8 on the sides with a large front (>1.))
Mention the switching condition - leader detects tight area or half of followers do, which prevents switching back formation until half of the robots are out of the corridor
Decentralized case only based on leader’s detection

## Slide 17: Insert video 6
Notes: Video shows everything
Split and merge, formation switching to column (safety formation), a tight corner, and a new obstacle (it’s adaptive)

## Slide 18
Centralized
Centralized vs decentralized example
Decentralized

## Slide 19: Results
Accuracy
  Error plot of distance to target with 5% noise
Decentralized
Centralized
Notes: Talk about accuracy as the error to the target position
Added 5% noise to velocity - simulates erroneous readings in position and sensors as well as handling minima
Centralized solution only has major spike during second set of denser obstacles but still looks nice, decentralized clearly less robust yet still functional

## Slide 20: Results
Robustness - Our general approach isn’t perfect
  Centralized obstacle avoidance is improved with global knowledge
  Decentralized solution not to the same level with just knowledge of leader
Efficiency - RRT* can take a long time so we precompute paths
Notes: Talk about robustness and some cases being sub-ideal due to obstacle avoidance - maybe reference motion in a video
RRT* can take on the order of minutes which is not ideal, storing precomputed paths is nice

## Slide 21: Results
Future Work
  Try cheaper straight-line goal velocities, rely on obstacle avoidance
  Improve obstacle avoidance to improve robustness in the general case
    Consider reinforcement learning to adjust weights for each environment
  Decentralized approach - communicate more state from each robot
Notes: Cheaper goal velocities and rely on obstacle avoidance velocities
Better obstacle avoidance to reduce error
Improve decentralized approach that stores the state of every robot, can then apply robot avoidance weights and better obstacle avoidance

## Slide 22
Link to code repository - github.com/DoodleBobBuffPants/RobotProject
Notes: Formation switching and navigation with tight corridors and multiple formations
Concluding remarks - can perform formation-based movement, but general robustness isn’t easy, and it’s easily decentralized
Mention where the code can be found